## Slide 1
10520 CS410001 - Computer Architecture 2017
Project #3
Project Objective
  Based on the single-cycled CPU simulator from project #1, implement a MIPS CPU simulator with memory hierarchy, Translation-Lookaside Buffer (TLB), and virtual page
table mechanism. The memory size, page size, cache total size, block size and set associativity of the cache should be configurable.
  Design and submit your own test case to verify the functionality of the memory hierarchy configuration.
Project Description
The simulator is similar to that of project 1 except the following:
  Name the executable CMP (which stands for Cache_Memory_Page_table).
  All data accesses from instructions are using virtual addressing
  Both instruction cache and data cache have only one level and your simulator should cover both caches.
  Cache Organization
i.
ii.
iii.
iv.
Both instruction cache and data cache adopt write-back/allocate policy.
The cache miss replacement policy for both caches: for the cache line under consideration, replace the least indexed invalid set if exists; otherwise, replace the
Bits-Pseudo LRU set. Details of Bits-Pseudo LRU can be found in Appendix E.
The default instruction cache is of 16 bytes, 4-way associative. The block size for
instruction cache is 4 bytes.
The default data cache is of 16 bytes, direct map. The block size for data cache is 4 bytes.
Cache Initialization
The valid bit of each cache block is set to be false before the simulation starts. All other contents are initialized as “don’t care” (x’s).
TLB Organization
i.
ii.
iii.
There should be two TLBs, one for IPageTable and one for DPageTable.
The TLBs is fully-associative and its size is a quarter of the page table size, i.e.,
#TLB_entries = 1/4*(#page_table_entries).
TLBs adopt the LRU replacement policy. In other words, replace the least indexed invalid entry if exists; otherwise, replace the LRU entry.
g. TLB Initialization
The valid bit of each page table block is initialized to be false before simulation begins. All other contents are “don’t care” (x’s).

## Slide 2
10520 CS410001 - Computer Architecture 2017
h. Page Table Organization
i.
ii. iii. iv.
Although theoretically we should have page table cover full 32-bit virtual space, for simplicity of verification you are required to calculate the page table size from the given disk size specified in this project, i.e.,
#page_table_entries = disk_size / page_size.
You have to map virtual address (VA) to physical address (PA)
At page fault, we assume that the virtual address (VA) is exactly the disk address.
The default instruction page size is 8 bytes and the default data page size is 16 bytes.
Page Table Initialization
The valid bit of each page table block is initialized to be false before simulation begins. All other contents are “don’t care” (x’s).
Memory Organization
i.
ii.
iii.
Both instruction memory and data memory adopt write-back/allocate policy. Memory replacement policy for page faults: If memory space is available, place data to the first available page closest to the page #0; otherwise, replace the LRU set. Pick the least indexed set to be the victim in case of tie.
The default instruction memory size is of 64 bytes and the default data memory
size is of 32 bytes.
Memory Initialization
All initial memory contents are 0x00000000h.
Disk Initialization
i.
ii.
Assume that both the instruction disk and data disk are of 1K bytes size.
All other memory contents whose addresses not specified by the image file are assumed to be of value 0x00000000h.
m. Configurability
The executable takes arguments from the command line. All size related parameters should be of power of two, and the exponent should be great than 1 (2n, n > 1). Note that if no command line parameters are set, the default configuration is taken for simulation. Other specifications are the same as project_1.pdf. The parameters should be of the following order:
i.
ii. iii. iv.
v.
vi. vii.
The instruction memory (I memory) size, in number of bytes The data memory (D memory) size, in number of bytes
The page size of instruction memory (I memory), in number of bytes The page size of data memory (D memory), in number of bytes
The total size of instruction cache (I cache), in number of bytes The block size of I cache, in number of bytes
The set associativity of I cache

## Slide 3
10520 CS410001 - Computer Architecture 2017
viii. ix.
x.
The total size of data cache (D cache), in number of bytes The block size of D cache, in number of bytes
The set associativity of D cache
Input and Output Format
Input: Same as that of Project 1. Please refer to the specification of Project 1 and Appendix B, “Sample Input.”
Output: For each test case, report.rpt and snapshot.rpt should be generated.
  snapshot.rpt
The requirement is the same as that for project 1. Please refer to project_1 and Appendix C-1, “Sample Output for Project 1.”
  report.rpt:
    For details please refer to Appendix C-3, “Sample Output for Project 3.”
    report.rpt should contain the following information for total memory access: total hit
/miss number of I-cache, D-cache, I-pagetable, D-pagetable, I-TLB, D-TLB.
Test Case Design
  Design a test case for the default configuration or other legal configuration to verify if your simulator handles every cache event correctly.
  The following testcases are invalid:
i.
ii. iii.
i-memory & d-memory address overflow i-memory & d-memory misaligned Simulation cycles over 500,000
Modularization
On top of the same design of Project 1, you can add a file named (ex:cmp.c) to implement your cache, TLB, page table related functions.
Grading Policy
  Mostly are same as Project 1, with each testcase (open, hidden, student testcase) testing with
three different configurations: default configuration and two other configurations.
i.
ii. iii.
10% discount if you fail one of them 19% discount if you fail both of them 0 point if you fail all of them
b. Demo will focus on:
i.
ii. iii.
Detail design of your program
Basic organization of TLB, page table, and memory Project report

## Slide 4
10520 CS410001 - Computer Architecture 2017
Etiquette
  Do not plagiarize others’ works, or you will fail this course.
  No acceptance of late homework.
  Please constantly check the class website announcements for any possible updates.